## Beginnings of a document on random

P4 optimizations and insights

Those considering assembly language optimizations on the P4 should first read the Intel manuals at

http://developer.intel.com/design/Pentium4/manuals/ especially the Processor Optimization Reference manual at http://developer.intel.com/design/pentium4/manuals/248966.htm.

Each section tries to analyze one small aspect of the P4 architecture.  It is followed by a conclusion or speculation regarding the observed behavior.  Often, these test cases raise more questions than they answer.

Each code snipet is timed in a loop of at least 100 iterations.  Memory is aligned on a 4KB page boundary.  The code is then run 200 times and the best timing is reported.  Note my machine is a 1.4 GHz P4 with PC600 memory (theoretical bandwidth of 2.4 GB/sec).  Note:  I’ve recently been told that the peak bandwidth for PC600 memory is 2.0 GB/sec (that is, PC600 is in reality PC512 memory!).  I’m trying to track down a reference for this, so far unsuccessfully.

Note, the Intel manuals sometimes refer to cache line size as 128 bytes and sometimes as 64 bytes.  In the examples below I’ll refer to a cache line as 64 bytes.  The L1 cache line size is 64 bytes.  The L2 cache is kind of a hybrid 128/64 byte cache.  A cache line fill reads 128 bytes, but my tests show that the L2 cache maintains separate dirty bits for each 64-byte chunk.

# Reading contiguous data

This code reads a contiguous block of memory using 4 bytes at a time.  Timings are done on 3 memory size.  4KB will read from the L1 cache only, 64KB will read from the L2 cache only, and 1MB will test reading from main memory.

mem = 4096            ; Read 4KB

cnt = mem/64          ; Read 64 bytes per iteration

mov     ecx, cnt

loop1:  mov     eax, [esi]              ; Read one cache line

mov     eax, [esi+4]			; 4 bytes at a time

mov     eax, [esi+8]

mov     eax, [esi+12]

mov     eax, [esi+16]

mov     eax, [esi+20]

mov     eax, [esi+24]

mov     eax, [esi+28]

mov     eax, [esi+32]

mov     eax, [esi+36]

mov     eax, [esi+40]

mov     eax, [esi+44]

mov     eax, [esi+48]

mov     eax, [esi+52]

mov     eax, [esi+56]

mov     eax, [esi+60]

lea     esi, [esi+64]			; Next cache line

sub     ecx, 1

jnz     loop1

lea     esi, [esi-mem]		; Restore esi

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Mem | Clocks | Clocks per loop iteration | Bandwidth | Comments |
| --- | --- | --- | --- | --- |
| 4096 (4KB) | 1037 | 16.2 | 5.53GB/sec | The expected result |
| 65536 (64KB) | 23625 | 23.07 | 3.88GB/sec | Any good theories here? |
| 1048576 (1MB) | 1180000 | 72.02 | 1.24GB/sec | 50% of theoretical throughput. Why? |

Now using MMX instructions:

mem = 4096                      ; Read 4KB

cnt = mem/64                    ; 64 bytes per iteration

mov     ecx, cnt

loop1:  movq    mm1, [esi]			; Read one cache line

movq    mm1, [esi+8]			; 8 bytes at a time

movq    mm1, [esi+16]

movq    mm1, [esi+24]

movq    mm1, [esi+32]

movq    mm1, [esi+40]

movq    mm1, [esi+48]

movq    mm1, [esi+56]

lea     esi, [esi+64]			; Next cache line

sub     ecx, 1

jnz     loop1

lea     esi, [esi-mem]

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Mem | Clocks | Clocks per loop iteration | Bandwidth | Comments |
| --- | --- | --- | --- | --- |
| 4096 (4KB) | 523 | 8.17 | 10.96GB/sec | As expected. |
| 65536 (64KB) | 15395 | 15.03 | 5.96GB/sec |  |
| 1048576 (1MB) | 1036299 | 63.25 | 1.42GB/sec | Still not theoretical throughput. Why? |

Now using XMM instructions:

mem = 4096                      ; Read 4KB

cnt = mem/64                    ; 64 bytes per iteration

mov     ecx, cnt

loop1:  movapd  xmm1, [esi]			; Read one cache line

movapd  xmm1, [esi+16]		; 16 bytes at a time

movapd  xmm1, [esi+32]

movapd  xmm1, [esi+48]

lea     esi, [esi+64]			; Next cache line

sub     ecx, 1

jnz     loop1

lea     esi, [esi-mem]

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Mem | Clocks | Clocks per loop iteration | Bandwidth | Comments |
| --- | --- | --- | --- | --- |
| 4096 (4KB) | 268 | 4.19 | 21.40GB/sec |  |
| 65536 (64KB) | 7766 | 7.58 | 11.81GB/sec |  |
| 1048576 (1MB) | 817776 | 49.91 | 1.80GB/sec | Still not theoretical throughput. Why? |

Conclusions:  The P4 is unable to hide all the latencies when reading from the L2 cache.  This is somewhat surprising, as it should be getting near perfect branch prediction.  Also, how does Intel justify claims of 44.8GB/sec for L2 cache bandwidth?

One would hope that the P4 would get closer to its 2.4GB/sec peak bandwidth.  Why isn’t it?

Now we will see if using the SSE2 prefetch instructions can get us closer to the 2.4GB/sec theoretical bandwidth.  We’ll also see how much as a performance penalty prefetch incurs when reading from the L2 cache.

mem = 16*16*4096                ; Read 1MB

pages = mem/4096                ; Number of 4KB pages

mov     ecx, pages

sub     ebx, ebx

loop0:  mov     eax, [esi+4096]         ; Preload next page TLB

loop1:  movapd  xmm1, [esi]             ; Read 2 cache lines

movapd  xmm1, [esi+16]          ; 16 bytes at a time

movapd  xmm1, [esi+32]

movapd  xmm1, [esi+48]

movapd  xmm1, [esi+64]

movapd  xmm1, [esi+80]

movapd  xmm1, [esi+96]

movapd  xmm1, [esi+112]

prefetcht1 [esi+4096]           ; Preload 2 lines in next page

lea     esi, [esi+128]          ; Next 2 cache lines

add     bl, 256/32              ; 32 iterations per page

jnc     loop1

sub     ecx, 1

jnz     loop0

lea     esi, [esi-mem]

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Mem | Clocks | Clocks per 64 byte cache line | Bandwidth | Comments |
| --- | --- | --- | --- | --- |
| 65536 (64KB) | 8602 | 8.40 | 10.67GB/sec | Unnecessary prefetch causes some overhead |
| 1048576 (1MB) | 737952 | 45.04 | 1.99GB/sec | Still not theoretical throughput. Why? |

Conclusions: The prefetch instruction caused a modest 11% overhead (8602 vs. 7766 clocks) when not reading from memory.  This overhead may well disappear in real-world code where the loop is actually doing real work.

# Reading non-contiguous data

This example reads an entire block of memory, but in a non-contiguous fashion.

mem = 4096                      ; Read 4KB

cnt = mem/(4*128)               ; 128 bytes per iteration

dist = 64

sub     ebx, ebx

mov     ecx, cnt

loop1:  movapd  xmm1, [esi+0*dist]      ; Read 8 cache lines

movapd  xmm1, [esi+1*dist]

movapd  xmm1, [esi+2*dist]

movapd  xmm1, [esi+3*dist]

movapd  xmm1, [esi+4*dist]

movapd  xmm1, [esi+5*dist]

movapd  xmm1, [esi+6*dist]

movapd  xmm1, [esi+7*dist]

lea     esi, [esi+16]           ; Same 8 cache lines

add     bl, 256/4			; 4 inner loop iterations

jnc     loop1

lea     esi, [esi-4*16+8*dist]  ; Next set of 8 cache lines

sub     ecx, 1

jnz     loop1

lea     esi, [esi-mem]

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Mem | Clocks | Clocks per 64 byte cache line | Bandwidth | Comments |
| --- | --- | --- | --- | --- |
| 4096 (4KB) | 268 | 4.19 | 21.40GB/sec | Same as contiguous |
| 65536 (64KB) | 5900 | 5.76 | 15.55GB/sec | Much faster! |
| 1048576 (1MB) | 818193 | 49.94 | 1.80GB/sec | Same as contiguous |

Conclusions:  This is very interesting.  If your application’s data fits in the L2 cache, grouping your L1 cache misses together increases your throughput.  You may want to try preloading L2 cache lines into the L1 cache in an earlier iteration.  For example, adding the line

mov     eax, [esi+512]          ; Preload line into L1 cache

in the contiguous read code speeds up the 64KB timing.  Also, if your application uses prefetcht1 to preload L2 cache lines and your application is not limited by main memory bandwidth, then preloading lines into the L1 cache could speed up your application.

# Writing contiguous data

mem = 4096                      ; Write 4KB

cnt = mem/64                    ; 64 bytes per iteration

mov     ecx, cnt

loop1:  movapd  [esi], xmm1			; Write one cache line

movapd  [esi+16], xmm1		; 16 bytes at a time

movapd  [esi+32], xmm1

movapd  [esi+48], xmm1

lea     esi, [esi+64]			; Next cache line

sub     ecx, 1

jnz     loop1

lea     esi, [esi-mem]

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Mem | Clocks | Clocks per 64 byte cache line | Bandwidth | Comments |
| --- | --- | --- | --- | --- |
| 4096 (4KB) | 902 | 14.09 | 6.36GB/sec | Slower than reading |
| 65536 (64KB) | 14372 | 14.04 | 6.38GB/sec | Slower than reading. |
| 1048576 (1MB) | 1768230 | 107.92 | 0.83GB/sec |  |

Conclusions:  The write-through L1 cache is a killer here.  It takes 14 clocks to write the L1 cache line back to the L2 cache.  This places a limit on how fast you can code an application that reads and writes

only from the L1 and L2 cache.  To keep the CPU fully working you must find 14 clocks of work to do for each 64 bytes your program writes.  Clearly, the writes to the L2 cache are not pipelined.

The main memory benchmark is also interesting.  Obviously, the processor needs to read the cache line from memory before doing the write operation.  The theoretical maximum bandwidth is thus 1.2GB/sec.  This example achieves only 66% of theoretical, while the contiguous read example achieves 75% of theoretical.  Why?

Now let’s try it using the movntpd instruction.  This should avoid the reading of the cache line prior to writing the cache line.

mem = 4096                      ; Write 4KB

cnt = mem/64                    ; 64 bytes per iteration

mov     ecx, cnt

loop1:  movntpd  [esi], xmm1			; Write one cache line

movntpd  [esi+16], xmm1		; 16 bytes at a time

movntpd  [esi+32], xmm1

movntpd  [esi+48], xmm1

lea     esi, [esi+64]			; Next cache line

sub     ecx, 1

jnz     loop1

lea     esi, [esi-mem]

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Mem | Clocks | Clocks per 64 byte cache line | Bandwidth | Comments |
| --- | --- | --- | --- | --- |
| 65536 (64KB) | 45052 | 44.00 | 2.03GB/sec | Slower, but see conclusions. |
| 1048576 (1MB) | 722035 | 44.07 | 2.03GB/sec |  |

Conclusions:  At first glance, the L2 cache test run looks slower than the movapd case.  This is misleading.  Using the movapd instruction left the L2 full of dirty cache lines that must one day be written to main memory.  What’s worse is the cache lines written to the L2 cache may have ousted other cache lines that might have been used in the future.  These dirty cache lines will slow down future cache line reads (the cache line will need to be written before the new cache line can be read in).  So, use movntpd for those cases where you truly will not be using the data in the future.

The main memory benchmark is also interesting.  I can find no reason why this should be faster than the read contiguous data case, but it is.  Why?

# Writing non-contiguous data

mem = 4096                      ; Write 4KB

cnt = mem/(4*128)               ; 128 bytes per iteration

dist = 64

sub     ebx, ebx

mov     ecx, cnt

loop1:  movapd  [esi+0*dist], xmm1      ; Write 8 cache lines

movapd  [esi+1*dist], xmm1

movapd  [esi+2*dist], xmm1

movapd  [esi+3*dist], xmm1

movapd  [esi+4*dist], xmm1

movapd  [esi+5*dist], xmm1

movapd  [esi+6*dist], xmm1

movapd  [esi+7*dist], xmm1

lea     esi, [esi+16]           ; Same cache lines

add     bl, 256/4			; 4 inner loop iterations

jnc     loop1

lea     esi, [esi-4*16+8*dist]  ; Next set of 8 cache lines

sub     ecx, 1

jnz     loop1

lea     esi, [esi-mem]

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Mem | Clocks | Clocks per iteration | Bandwidth | Comments |
| --- | --- | --- | --- | --- |
| 4096 (4KB) | 2845 | 88.25 | 2.02GB/sec | Much slower than contiguous writes |
| 65536 (64KB) | 45516 | 88.25 | 2.02GB/sec | Also slower than contiguous case. |
| 1048576 (1MB) | 1957866 | 239.00 | 0.75GB/sec | Slower than reading. Why? |

Conclusions:  Group your writes together!!!  Failure to do so reduces throughput by 66%.  Here each cache-line write takes 11 clocks instead of 14 in the contiguous case.  This test below will tell us if write-combining is helping to some degree.

Now we’ll do the same as above, but only writing to 16 bytes in each cache line.

mem = 4096                      ; Write 4KB

cnt = mem/(8*64)                ; 8 cache lines each iteration

dist = 64

mov     ecx, cnt

loop1:  movapd  [esi+0*dist], xmm1      ; Write 8 cache lines

movapd  [esi+1*dist], xmm1

movapd  [esi+2*dist], xmm1

movapd  [esi+3*dist], xmm1

movapd  [esi+4*dist], xmm1

movapd  [esi+5*dist], xmm1

movapd  [esi+6*dist], xmm1

movapd  [esi+7*dist], xmm1

lea     esi, [esi+8*dist]       ; Next set of 8 cache lines

sub     ecx, 1

jnz     loop1

lea     esi, [esi-mem]

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Mem | Clocks | Clocks per iteration | Comments |
| --- | --- | --- | --- |
| 4096 (4KB) | 706 | 88.25 | Same as timing above |

Conclusions:  This indicates that each write takes 11 clocks.  Write-combining was of no value in the previous benchmark.  I speculate the 14 clocks in the contiguous write case is broken down as follows, 11 for the write to L2 cache and 1 clock for each of the 3 movapd write-combinings that took place.

# Cost of a TLB miss

This code reads one cache line from each 4KB page.  The L1 and L2 cache line collisions are minimized so that we can analyze the cost of a TLB miss.

tlbs = 32

cnt = tlbs/8

mov     ecx, cnt

sub     eax, eax

loop1:  movapd  xmm1, [esi]             ; Read from a 4KB page

lea     esi, [esi+4096+64]      ; Different line, next page

add     al, 256/8               ; 8 inner loops - for

jnc     loop1				; perfect branch prediction

sub     ecx, 1

jnz     loop1

lea     esi, [esi-tlbs*(4096+64)]

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Tlbs | Clocks | Clocks per TLB | Comments |
| --- | --- | --- | --- |
| 32 | 82 | 2.56 |  |
| 64 | 147 | 2.3 | Timings vary widely |
| 72 | 357 | 4.95 | TLB miss penalty starting to kick in |
| 128 | 2608 | 20.38 | Should be no TLB hits |

Conclusion:  A TLB miss where the page table entry is in the L2 cache costs 18 clocks.

# Real world programs – reading and writing contiguous data

The above examples are nice, but most applications read data, operate on it, and write it back.

mem = 4096                      ; Work on 4KB

cnt = mem/64                    ; 64 bytes per iteration

mov     ecx, cnt

loop1:  movapd  xmm0, [esi]             ; Read one cache line

movapd  xmm1, [esi+16]

movapd  xmm2, [esi+32]

movapd  xmm3, [esi+48]

subpd   xmm0, xmm0              ; Operate on the data

pxor    xmm1, xmm1

subpd   xmm2, xmm2

pxor    xmm3, xmm3

movapd  [esi], xmm0             ; Write the cache line

movapd  [esi+16], xmm1

movapd  [esi+32], xmm2

movapd  [esi+48], xmm3

lea     esi, [esi+64]           ; Next cache line

sub     ecx, 1

jnz     loop1

lea     esi, [esi-mem]

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Mem | Clocks | Clocks per 64 byte cache line | Bandwidth | Comments |
| --- | --- | --- | --- | --- |
| 4096 (4KB) | 901 | 14.07 | 6.36GB/sec | Limited by write-through to L2 speed |
| 65536 (64KB) | 24669 | 24.09 | 3.72GB/sec |  |
| 1048576 (1MB) | 1893992 | 115.60 | 0.78GB/sec |  |

Conclusions:  We need a good explanation for the 24 clock number in the L2 cache timing.  Ideas?

If you want to write a program that is CPU bound instead of memory bandwidth bound, you must perform at least 116 clocks of ALU/FPU instructions for every 64 bytes read!  Obviously, it is very difficult to do this for applications whose data does not fit in the L2 cache.

Now let’s try replacing the last 4 movapd instructions with movntpd:

| Mem | Clocks | Clocks per 64 byte cache line | Bandwidth | Comments |
| --- | --- | --- | --- | --- |
| 1048576 (1MB) | 1822550 | 111.24 | 0.81GB/sec |  |

Conclusion:  Not much difference.  This could be within our margin of error in timing or it could indicate that there is a slight penalty for reading into a dirty cache line as opposed to writing dirty cache lines immediately.  Warning: Even though this benchmark suggests using movntpd, using movapd is probably advantageous.  In programs that are not limited by memory bandwidth, you may well be able to completely hide the write time by using prefetch instructions.  Just be aware in scheduling your prefetch instructions that the cache line you are reading may force a write prior to the read.

In coding one application, I thought it would be advantageous to use the clflush instruction to write out dirty cache lines during a period where the program was CPU bound (a kind of prefetcht1 instruction in reverse!)  This turned out to be a losing move.  Adding a “clflush [esi]” instruction after the 4 write instructions balloons the timing to 2625967 clocks.  Avoid clflush at all costs.

Now what happens when we read from one area of memory and write to another:

mem = 1048576                   ; Work on 1MB

cnt = mem/64                    ; 64 bytes per iteration

mov     ecx, cnt

loop1:  movapd  xmm0, [esi]             ; Read one cache line

movapd  xmm1, [esi+16]

movapd  xmm2, [esi+32]

movapd  xmm3, [esi+48]

subpd   xmm0, xmm0              ; Operate on the data

pxor    xmm1, xmm1

subpd   xmm2, xmm2

pxor    xmm3, xmm3

movntpd  [esi+mem], xmm0        ; Write the cache line

movntpd  [esi+mem+16], xmm1

movntpd  [esi+mem+32], xmm2

movntpd  [esi+mem+48], xmm3

lea     esi, [esi+64]           ; Next cache line

sub     ecx, 1

jnz     loop1

lea     esi, [esi-mem]

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Mem | Clocks | Clocks per 64 byte cache line | Bandwidth | Comments |
| --- | --- | --- | --- | --- |
| 1048576 (1MB) | 1680771 | 102.59 | 0.87GB/sec |  |

Conclusions:  Why is this 10% faster than writing to the cache line just read in?

# A real world program – fast Fourier transform on a huge data set

I run a distributed computing search for large prime numbers at http://www.mersenne.org/prime.htm.  The program performs fast Fourier transforms on large data sets (up to 4 million doubles – 32MB of data).  The present program is all assembly language and needs to be upgraded with p4 optimized code.  Using SSE2 instructions and being mindful of  P4 cache considerations should yield a threefold performance boost.  Hopefully, what I learn in constructing the basic building blocks of this FFT will yield some insights useful to other P4 assembly language programmers.

All you need to know about fast Fourier transforms is they perform a ton of floating point operations in a regular, but non-contiguous data access pattern.

We will analyze using the variations of the macro below.  What it does is unimportant.  It reads 8 XMM registers from 8 different cache lines, does stuff, and writes the new values back.  Since it does 20 addpd and subpd instructions, a best case timing is 40 clocks.

test_macro MACRO R1,R2,R3,R4,R5,R6,R7,R8

movapd  xmm0, R4                ;; R4

movapd  xmm1, R8                ;; R8

subpd   xmm0, xmm1              ;; new R8 = R4 - R8

movapd  xmm2, R2                ;; R2

movapd  xmm3, R6                ;; R6

subpd   xmm2, xmm3              ;; new R6 = R2 - R6

addpd   xmm1, R4                ;; new R4 = R4 + R8

movapd xmm7, XMM_SQRTHALF      ;; square root of 1/2

mulpd  xmm0, xmm7              ;; R8 = R8 * square root

addpd   xmm3, R2                ;; new R2 = R2 + R6

mulpd  xmm2, xmm7              ;; R6 = R6 * square root

movapd  xmm4, R1                ;; R1

movapd  xmm5, R5                ;; R5

addpd   xmm5, xmm4              ;; new R1 = R1 + R5

subpd  xmm3, xmm1              ;; R2 = R2 - R4 (final R4)

multwo xmm1                    ;; R4 = R4 * 2

movapd  xmm6, R3                ;; R3

movapd  xmm7, R7                ;; R7

addpd   xmm7, xmm6              ;; new R3 = R3 + R7

subpd  xmm2, xmm0              ;; R6 = R6 - R8 (Real part)

multwo xmm0                    ;; R8 = R8 * 2

subpd  xmm5, xmm7              ;; R1 = R1 - R3 (final R3)

multwo xmm7                    ;; R3 = R3 * 2

subpd   xmm4, R5                ;; new R5 = R1 - R5

addpd  xmm1, xmm3              ;; R4 = R2 + R4 (new R2)

addpd   xmm0, xmm2              ;; R8 = R6 + R8 (Imag. part)

subpd   xmm4, xmm2              ;; R5 = R5 - R6 (final R7)

multwo  xmm2                    ;; R6 = R6 * 2

subpd   xmm6, R7                ;; new R7 = R3 - R7

addpd  xmm7, xmm5              ;; R3 = R1 + R3 (new R1)

subpd   xmm6, xmm0              ;; R7 = R7 - R8 (final R8)

multwo  xmm0                    ;; R8 = R8 * 2

subpd   xmm7, xmm1              ;; R1 = R1 - R2 (final R2)

multwo  xmm1                    ;; R2 = R2 * 2

movapd  R4, xmm3

movapd  R3, xmm5

addpd   xmm2, xmm4              ;; R6 = R5 + R6 (final R5)

addpd   xmm0, xmm6              ;; R8 = R7 + R8 (final R6)

addpd   xmm1, xmm7              ;; R2 = R1 + R2 (final R1)

movapd  R7, xmm4

movapd  R8, xmm6

movapd  R2, xmm7

movapd  R5, xmm2

movapd  R6, xmm0

movapd  R1, xmm1

ENDM

test_disp MACRO mac, s, d1, d2, d4

mac [s],[s+d1],[s+d2],[s+d2+d1],[s+d4],[s+d4+d1],[s+d4+d2],[s+d4+d2+d1]

ENDM

multwo  MACRO   r

mulpd   r, XMM_TWO

ENDM

I time the above macro 3 ways, using 128 bytes, 2KB, or 64KB.  The 128 bytes and 2KB timings should give best-case scenarios – operating out of the fast L1 cache.  The 2KB example will imitate the loop constructs typical in an FFT program. The 64KB example is more like how I’ll be using the macro – operating out of the L2 cache.

use_128_bytes:

mov     edx, macro_count

loop2:  test_disp test_macro, esi, 64, 128, 256

sub     edx, 1                  ; Check loop counter

jnz     loop2                   ; Loop if necessary

use_2KB:

mov     edx, macro_count/16

sub     eax, eax

loop3:  test_disp test_macro, esi, 64, 128, 256

lea     esi, [esi+16]

add     al, 256/4               ; 4 XMMs per cache line

jnc     loop3

lea     esi, [esi-4*16+512]

add     ah, 256/4               ; 4 512-byte blocks in 2KB

jnc     loop3

lea     esi, [esi-4*512]

sub     edx, 1                  ; Check loop counter

jnz     loop3                   ; Loop if necessary

use_64KB:

mov     edx, macro_count/512

sub     eax, eax

loop4:  test_disp test_macro, esi, 64, 128, 256

lea     esi, [esi+16]

add     al, 256/4               ; 4 XMMs per cache line

jnc     loop4

lea     esi, [esi-4*16+512]

add     ah, 256/128             ; 128 512-byte blocks in 64KB

jnc     loop4

lea     esi, [esi-128*512]

sub     edx, 1                  ; Check loop counter

jnz     loop4                   ; Loop if necessary

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Bytes processed | Average clocks per test_macro | Comments |
| --- | --- | --- |
| 128 | 106.2 | Limited by write-through to L2 speed |
| 2KB | 88.8 |  |
| 64KB | 104.0 |  |

Conclusions:  No where near the 40 clocks we hoped for.  The 2KB case clearly seems limited by the 11 clocks per L1 write-through operation.  The 128 byte example is probably incurring some store-forwarding penalties.  The 64KB example is unable to hide the slower L2 cache latencies.  This might be due to using bandwidth for L1 write-throughs?

In any event, it seems my FFT cannot be an in-place FFT.  Fortunately, it is not hard to modify the code to read from 8 cache lines and write contiguously to a small memory block.  Then later read from the small memory block and write contiguously back to my FFT data area.

The new macro is as such:

test_macro MACRO dstreg,R1,R2,R3,R4,R5,R6,R7,R8

movapd  xmm0, R4                ;; R4

movapd  xmm1, R8                ;; R8

subpd   xmm0, xmm1              ;; new R8 = R4 - R8

movapd  xmm2, R2                ;; R2

movapd  xmm3, R6                ;; R6

subpd   xmm2, xmm3              ;; new R6 = R2 - R6

addpd   xmm1, R4                ;; new R4 = R4 + R8

movapd xmm7, XMM_SQRTHALF      ;; square root of 1/2

mulpd  xmm0, xmm7              ;; R8 = R8 * square root

addpd   xmm3, R2                ;; new R2 = R2 + R6

mulpd  xmm2, xmm7              ;; R6 = R6 * square root

movapd  xmm4, R1                ;; R1

movapd  xmm5, R5                ;; R5

addpd   xmm5, xmm4              ;; new R1 = R1 + R5

subpd  xmm3, xmm1              ;; R2 = R2 - R4 (final R4)

multwo xmm1                    ;; R4 = R4 * 2

movapd  xmm6, R3                ;; R3

movapd  xmm7, R7                ;; R7

addpd   xmm7, xmm6              ;; new R3 = R3 + R7

subpd  xmm2, xmm0              ;; R6 = R6 - R8 (Real part)

multwo xmm0                    ;; R8 = R8 * 2

subpd  xmm5, xmm7              ;; R1 = R1 - R3 (final R3)

multwo xmm7                    ;; R3 = R3 * 2

subpd   xmm4, R5                ;; new R5 = R1 - R5

addpd  xmm1, xmm3              ;; R4 = R2 + R4 (new R2)

addpd   xmm0, xmm2              ;; R8 = R6 + R8 (Imag. part)

subpd   xmm4, xmm2              ;; R5 = R5 - R6 (final R7)

multwo  xmm2                    ;; R6 = R6 * 2

subpd   xmm6, R7                ;; new R7 = R3 - R7

addpd  xmm7, xmm5              ;; R3 = R1 + R3 (new R1)

subpd   xmm6, xmm0              ;; R7 = R7 - R8 (final R8)

multwo  xmm0                    ;; R8 = R8 * 2

subpd   xmm7, xmm1              ;; R1 = R1 - R2 (final R2)

multwo  xmm1                    ;; R2 = R2 * 2

movapd  [dstreg+3*16], xmm3

movapd  [dstreg+2*16], xmm5

addpd   xmm2, xmm4              ;; R6 = R5 + R6 (final R5)

addpd   xmm0, xmm6              ;; R8 = R7 + R8 (final R6)

addpd   xmm1, xmm7              ;; R2 = R1 + R2 (final R1)

movapd  [dstreg+6*16], xmm4

movapd  [dstreg+7*16], xmm6

movapd  [dstreg+1*16], xmm7

movapd  [dstreg+4*16], xmm2

movapd  [dstreg+5*16], xmm0

movapd  [dstreg+0*16], xmm1

ENDM

test_disp MACRO mac, s, dst, d1, d2, d4

mac dst,[s],[s+d1],[s+d2],[s+d2+d1],[s+d4],[s+d4+d1],[s+d4+d2],[s+d4+d2+d1]

ENDM

use_128_bytes:

mov     edx, macro_count

loop2:  test_disp test_macro, esi, ebp, 64, 128, 256

sub     edx, 1                  ; Check loop counter

jnz     loop2                   ; Loop if necessary

use_2KB:

mov     edx, macro_count/16

sub     eax, eax

loop3:  test_disp test_macro, esi, ebp, 64, 128, 256

lea     esi, [esi+16]

lea     ebp, [ebp+128]

add     al, 256/4               ; 4 XMMs per cache line

jnc     loop3

lea     esi, [esi-4*16+512]

lea     ebp, [ebp-4*128]

add     ah, 256/4               ; 4 512-byte blocks in 2KB

jnc     loop3

lea     esi, [esi-4*512]

sub     edx, 1                  ; Check loop counter

jnz     loop3                   ; Loop if necessary

use_64KB:

mov     edx, macro_count/512

sub     eax, eax

loop4:  test_disp test_macro, esi, ebp, 64, 128, 256

lea     esi, [esi+16]

lea     ebp, [ebp+128]

add     al, 256/4               ; 4 XMMs per cache line

jnc     loop4

lea     esi, [esi-4*16+512]

lea     ebp, [ebp-4*128]

add     ah, 256/128             ; 128 512-byte blocks in 64KB

jnc     loop4

lea     esi, [esi-128*512]

sub     edx, 1                  ; Check loop counter

jnz     loop4                   ; Loop if necessary

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Bytes processed | Average clocks per test_macro | Comments |
| --- | --- | --- |
| 128 | 40.0 | Perfect! |
| 2KB | 40.0 | My funny looping constructs cost nothing! |
| 64KB | 45.9 | Still some work to be done. |

Conclusions:  Excellent progress – an impressive display by the P4 instruction scheduler.  We still need to work on ways to reduce the penalty of operating out of the L2 cache.

The following examples detail my attempts at reducing the 5.9 clock penalty.  Our earlier examples suggest preloading the cache lines into the L1 cache will be helpful.

use_64KB:

mov     edx, macro_count/512

sub     eax, eax

loop4:  test_disp test_macro, esi, ebp, 64, 128, 256

lea     esi, [esi+16]

lea     ebp, [ebp+128]

add     al, 256/4               ; 4 XMMs per cache line

jnc     loop4

mov	 ebx, [esi-4*16+512+512] ; Preload cache lines into L1

mov	 ebx, [esi-4*16+512+512+128]

mov	 ebx, [esi-4*16+512+512+256]

mov	 ebx, [esi-4*16+512+512+384]

mov	 ebx, [esi-4*16+512+512+64]

mov	 ebx, [esi-4*16+512+512+128+64]

mov	 ebx, [esi-4*16+512+512+256+64]

mov     ebx, [esi-4*16+512+512+384+64]

lea     esi, [esi-4*16+512]

lea     ebp, [ebp-4*128]

add     ah, 256/128             ; 128 512-byte blocks in 64KB

jnc     loop4

lea     esi, [esi-128*512]

sub     edx, 1                  ; Check loop counter

jnz     loop4                   ; Loop if necessary

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Bytes processed | Average clocks per test_macro | Comments |
| --- | --- | --- |
| 64KB | 45.9 | No change |

I next tried moving the

lea     esi, [esi+16]

as early as possible.  That is, after the

subpd   xmm6, R7                ;; new R7 = R3 - R7

instruction.  This should make little or no difference since the P4 should have no difficulty scheduling the lea instruction.  However, I wanted to give the processor every opportunity to schedule the preloads as soon as possible.

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Bytes processed | Average clocks per test_macro | Comments |
| --- | --- | --- |
| 64KB | 42.7 | Wow! A theoretically useless change saves 3 clocks |

Next I tried to distribute the L1 cache preloads more evenly at the cost of using another register.

use_64KB:

mov     edx, macro_count/512

sub     eax, eax

lea     ecx, [esi+640]          ; Preload 10 cache lines ahead

loop4:  test_disp test_macro, esi, ebp, 64, 128, 256

mov     ebx, [ecx]              ; Preload cache lines into L1

mov     ebx, [ecx+64]

lea     ecx, [ecx+128]

lea     esi, [esi+16]

lea     ebp, [ebp+128]

add     al, 256/4               ; 4 XMMs per cache line

jnc     loop4

lea     esi, [esi-4*16+512]

lea     ebp, [ebp-4*128]

add     ah, 256/128             ; 128 512-byte blocks in 64KB

jnc     loop4

lea     esi, [esi-128*512]

lea     ecx, [ecx-128*512]

sub     edx, 1                  ; Check loop counter

jnz     loop4                   ; Loop if necessary

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Bytes processed | Average clocks per test_macro | Comments |
| --- | --- | --- |
| 64KB | 41.1 | As coded above |
| 64KB | 40.9 | With “lea esi, [esi+16]” moved as described earlier |

Conclusions:  While I’ve not figured out a way to get the perfect 40.0 clocks, I have gotten close.  While I don’t have an explanation for the observed behavior, we can conclude that programs should endeavor to compute addresses as early as possible and preload the L1 cache if possible.

# A real world program – fast Fourier transform on a huge data set (continued)

We’ve shown that the most basic of FFT building locks can come very close to perfect scheduling running out of the L2 cache.  Now we’ll organize put together many executions of the test_macro building block that emulates how my FFT operates on 64KB of data.  We’ll test this running on the same 64KB over and over again as well as operating on contiguous 64KB blocks of main memory.  We hope to use prefetch to eliminate all waiting for main memory.

Note:  I’ve changed the test_macro below to accept an argument specifying how much the source register should be incremented.

test_macro MACRO srcreg,inc,dstreg,R1,R2,R3,R4,R5,R6,R7,R8

movapd  xmm0, R4                ;; R4

movapd  xmm1, R8                ;; R8

subpd   xmm0, xmm1              ;; new R8 = R4 - R8

movapd  xmm2, R2                ;; R2

movapd  xmm3, R6                ;; R6

subpd   xmm2, xmm3              ;; new R6 = R2 - R6

addpd   xmm1, R4                ;; new R4 = R4 + R8

movapd xmm7, XMM_SQRTHALF      ;; square root of 1/2

mulpd  xmm0, xmm7              ;; R8 = R8 * square root

addpd   xmm3, R2                ;; new R2 = R2 + R6

mulpd  xmm2, xmm7              ;; R6 = R6 * square root

movapd  xmm4, R1                ;; R1

movapd  xmm5, R5                ;; R5

addpd   xmm5, xmm4              ;; new R1 = R1 + R5

subpd  xmm3, xmm1              ;; R2 = R2 - R4 (final R4)

multwo xmm1                    ;; R4 = R4 * 2

movapd  xmm6, R3                ;; R3

movapd  xmm7, R7                ;; R7

addpd   xmm7, xmm6              ;; new R3 = R3 + R7

subpd  xmm2, xmm0              ;; R6 = R6 - R8 (Real part)

multwo xmm0                    ;; R8 = R8 * 2

subpd  xmm5, xmm7              ;; R1 = R1 - R3 (final R3)

multwo xmm7                    ;; R3 = R3 * 2

subpd   xmm4, R5                ;; new R5 = R1 - R5

addpd  xmm1, xmm3              ;; R4 = R2 + R4 (new R2)

addpd   xmm0, xmm2              ;; R8 = R6 + R8 (Imag. part)

subpd   xmm4, xmm2              ;; R5 = R5 - R6 (final R7)

multwo  xmm2                    ;; R6 = R6 * 2

subpd   xmm6, R7                ;; new R7 = R3 - R7

IF inc NE 0

add     srcreg, inc

ENDIF

addpd  xmm7, xmm5              ;; R3 = R1 + R3 (new R1)

subpd   xmm6, xmm0              ;; R7 = R7 - R8 (final R8)

multwo  xmm0                    ;; R8 = R8 * 2

subpd   xmm7, xmm1              ;; R1 = R1 - R2 (final R2)

multwo  xmm1                    ;; R2 = R2 * 2

addpd   xmm2, xmm4              ;; R6 = R5 + R6 (final R5)

addpd   xmm0, xmm6              ;; R8 = R7 + R8 (final R6)

addpd   xmm1, xmm7              ;; R2 = R1 + R2 (final R1)

movapd  [dstreg+0*16], xmm1

movapd  [dstreg+1*16], xmm7

movapd  [dstreg+2*16], xmm5

movapd  [dstreg+3*16], xmm3

movapd  [dstreg+4*16], xmm2

movapd  [dstreg+5*16], xmm0

movapd  [dstreg+6*16], xmm4

movapd  [dstreg+7*16], xmm6

ENDM

test_disp MACRO mac, s, inc, dst, d1, d2, d4

mac s,inc,dst,[s],[s+d1],[s+d2],[s+d2+d1],[s+d4],[s+d4+d1],[s+d4+d2],[s+d4+d2+d1]

ENDM

Here’s the new macro that executes the above macro 4608 times. Don’t worry about the details too much.  All you really need to know is it executes the macro 512 times in place, then 4 times it executes the macro 1024 times – copying data to a small scratch area and back to the source area.

xpass2 MACRO

LOCAL   b1b, b2a, b2b, b3b, b4a, b4b, b5b

LOCAL   b6a, b6b, b7b, b8a, b8b, b9b, bab

sub	ecx, ecx

; FFT levels 1-2 in place

mov     eax, 512                ;; 512 iterations

b1b:    test_disp test_macro, esi, 0, esi, 16, 32, 64

lea     esi, [esi+128]

sub     eax, 1                  ;; Test inner loop counter

jnz     b1b                     ;; Iterate if necessary

; FFT levels 3-4 to scratch area

lea     esi, [esi-512*128]      ;; Next source pointer

b2a:    mov     ebp, OFFSET XMM_SCRATCH_AREA

b2b:    test_disp test_macro, esi, 32, ebp, 16, 256, 512

lea     ebp, [ebp+128]

add     al, 256/4               ;; Test inner loop counter

jnc     b2b                     ;; Iterate if necessary

lea     esi, [esi-4*32+4*256]   ;; Next source pointer

add     ah, 256/4               ;; Test inner loop counter

jnc     b2b                     ;; Iterate if necessary

; FFT levels 5-6 from scratch area

lea     esi, [esi-16*256]       ;; Next source pointer

mov     ebp, OFFSET XMM_SCRATCH_AREA

b3b:    test_disp test_macro, ebp, 128, esi, 16, 32, 64

lea     esi, [esi+256]

add     al, 256/16

jnc     b3b

add     cl, 256/16              ;; 16 iterations

jnc     b2a                     ;; Iterate if necessary

lea     esi, [esi-256*256+128]  ;; Next source pointer

add     ch, 256/2               ;; 2 iterations

jnc     b2a                     ;; Iterate if necessary

; FFT levels 7-8 to scratch area

lea     esi, [esi-2*128]        ;; Next source pointer

b4a:    mov     ebp, OFFSET XMM_SCRATCH_AREA

b4b:    test_disp test_macro, esi, 32, ebp, 16, 256, 512

lea     ebp, [ebp+128]

add     al, 256/4               ;; Test inner loop counter

jnc     b4b                     ;; Iterate if necessary

lea     esi, [esi-4*32+4*256]   ;; Next source pointer

add     ah, 256/4               ;; Test inner loop counter

jnc     b4b                     ;; Iterate if necessary

; FFT levels 9-10 from scratch area

lea     esi, [esi-16*256]       ;; Next source pointer

mov     ebp, OFFSET XMM_SCRATCH_AREA

b5b:    test_disp test_macro, ebp, 128, esi, 16, 32, 64

lea     esi, [esi+256]

add     al, 256/16

jnc     b5b

add     cl, 256/16              ;; 16 iterations

jnc     b4a                     ;; Iterate if necessary

lea     esi, [esi-256*256+128]  ;; Next source pointer

add     ch, 256/2               ;; 2 iterations

jnc     b4a                     ;; Iterate if necessary

; FFT levels 7-8 to scratch area

lea     esi, [esi-2*128]        ;; Next source pointer

b6a:    mov     ebp, OFFSET XMM_SCRATCH_AREA

b6b:    test_disp test_macro, esi, 32, ebp, 16, 256, 512

lea     ebp, [ebp+128]

add     al, 256/4               ;; Test inner loop counter

jnc     b6b                     ;; Iterate if necessary

lea     esi, [esi-4*32+4*256]   ;; Next source pointer

add     ah, 256/4               ;; Test inner loop counter

jnc     b6b                     ;; Iterate if necessary

; FFT levels 5-6 from scratch area

lea     esi, [esi-16*256]       ;; Next source pointer

mov     ebp, OFFSET XMM_SCRATCH_AREA

b7b:    test_disp test_macro, ebp, 128, esi, 16, 32, 64

lea     esi, [esi+256]

add     al, 256/16

jnc     b7b

add     cl, 256/16              ;; 16 iterations

jnc     b6a                     ;; Iterate if necessary

lea     esi, [esi-256*256+128]  ;; Next source pointer

add     ch, 256/2               ;; 2 iterations

jnc     b6a                     ;; Iterate if necessary

; FFT levels 3-4 to scratch area

lea     esi, [esi-2*128]        ;; Next source pointer

b8a:    mov     ebp, OFFSET XMM_SCRATCH_AREA

b8b:    test_disp test_macro, esi, 32, ebp, 16, 256, 512

lea     ebp, [ebp+128]

add     al, 256/4               ;; Test inner loop counter

jnc     b8b                     ;; Iterate if necessary

lea     esi, [esi-4*32+4*256]   ;; Next source pointer

add     ah, 256/4               ;; Test inner loop counter

jnc     b8b                     ;; Iterate if necessary

; FFT levels 1-2 from scratch area

lea     esi, [esi-16*256]       ;; Next source pointer

mov     ebp, OFFSET XMM_SCRATCH_AREA

b9b:    test_disp test_macro, ebp, 128, esi, 16, 32, 64

lea     esi, [esi+256]

add     al, 256/16

jnc     b9b

add     cl, 256/16              ;; 16 iterations

jnc     b8a                     ;; Iterate if necessary

lea     esi, [esi-256*256+128]  ;; Next source pointer

add     ch, 256/2               ;; 2 iterations

jnc     b8a                     ;; Iterate if necessary

lea     esi, [esi-2*128]        ;; Restore source pointer

ENDM

The macro is timed two ways:

in_place:

mov     edx, 100

loop1:  xpass2

sub     edx, 1

jnz     loop1

main_memory:

mov     edx, 100

loop2:  xpass2

lea     esi, [esi+65536]

sub     edx, 1

jnz     loop2

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Memory access pattern | Clocks for each xpass2 | Clocks per 64 byte cache line processed | Clocks per test_macro call | Comments |
| --- | --- | --- | --- | --- |
| 64KB in place | 212780 | 207.8 | 46.2 | Close to expected |
| 64KB main mem. | 303935 | 296.8 | 66.0 |  |

Conclusion:  The 46.2 clocks per test_macro closely matches the timings above where the L1 cache was not preloaded.  Note that one-third of the test_macro calls (those operating from the small scratch area) should be operating on data in the L1 cache.  However, preloading the L1 cache for the other two-thirds of the test_macro calls may well get us close to the previous section’s 40.8 clocks.

Also, note the 89 clocks spent reading and writing main memory.  This makes sense as it translates to (64 bytes written + 64 bytes read) / 89 clocks * 1.4GHz = 2GB/sec.  Using prefetch, it should be possible to hide these 89 clocks among the 207.8 clocks of CPU activity.

Now we modify the in place section slightly allowing moving the computation of the new esi value earlier in the loop:

; FFT levels 1-2 in place

mov     eax, 512                ;; 512 iterations

mov     ebp, esi

b1b:    test_disp test_macro, esi, 128, ebp, 16, 32, 64

lea     ebp, [ebp+128]

sub     eax, 1                  ;; Test inner loop counter

jnz     b1b                     ;; Iterate if necessary

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Memory access pattern | Clocks for each xpass2 | Clocks per 64 byte cache line processed | Clocks per test_macro call | Comments |
| --- | --- | --- | --- | --- |
| 64KB in place | 207614 | 202.7 | 45.1 | Wow. |
| 64KB main mem. | 303349 | 296.2 | 65.8 |  |

Conclusion:  This is amazing.  The difference 5166 clock difference must come from the first 512 test_macro calls.  That means, there is a 10 clock benefit to using two addressing registers and computing the new source register value as soon as possible.

Something is fishy with the above result.  When we analyzed moving the lea instruction earlier we never saw a 10 clock benefit.  I tried several ideas before this rather startling discovery.  Add a nop here:

; FFT levels 7-8 to scratch area

nop

lea     esi, [esi-2*128]        ;; Next source pointer

b4a:    mov     ebp, OFFSET XMM_SCRATCH_AREA

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Memory access pattern | Clocks for each xpass2 | Clocks per 64 byte cache line processed | Clocks per test_macro call | Comments |
| --- | --- | --- | --- | --- |
| 64KB in place | 203266 | 198.5 | 44.1 | Wow. |
| 64KB main mem. | 300511 | 293.5 | 65.2 |  |

Conclusions:  Apparently there is an undocumented penalty dealing with code alignment!

Further investigation shows that if two jump instructions are 15 bytes apart and the first jump instruction starts on an odd address, then the BTB fails in predicting the second jump instruction.  When I replace the four occurrences of:

jnc     b8b                     ;; Iterate if necessary

lea     esi, [esi-4*32+4*256]   ;; Next source pointer

add     ah, 256/4               ;; Test inner loop counter

jnc     b8b                     ;; Iterate if necessary

with:

jnc     b8b                     ;; Iterate if necessary

nop

lea     esi, [esi-4*32+4*256]   ;; Next source pointer

add     ah, 256/4               ;; Test inner loop counter

jnc     b8b                     ;; Iterate if necessary

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Memory access pattern | Clocks for each xpass2 | Clocks per 64 byte cache line processed | Clocks per test_macro call | Comments |
| --- | --- | --- | --- | --- |
| 64KB in place | 199998 | 195.3 | 43.4 |  |
| 64KB main mem. | 297440 | 290.5 | 64.5 |  |

Conclusions:  Despite the P4 optimization manual saying that the P4 is less affected by code alignment than earlier processors, there are still circumstances where code alignment can have a major impact on performance.

However, my findings above are pretty weird.  I can’t imagine a design decision Intel could have made that would result in the 15-byte even/odd anomaly.  Obviously, more research is needed on the implications of the P4’s branch prediction algorithm.

Now, we’ll try to use prefetch to reduce the main memory timing.  Here is my first attempt:

xpass2 MACRO

LOCAL   b1b, b2a, b2b, b3b, b4a, b4b, b5b

LOCAL   b6a, b6b, b7b, b8a, b8b, b9b, bab

sub     ecx, ecx

;; Touch the TLBs we are about to FFT so they are marked most

;; recently used. Then load the TLBs for the next 64KB FFT chunk

;; so that prefetcht1 works.

bab:    mov     eax, [esi]

lea     esi, [esi+4096]         ;; Next page

add     cl, 256/32              ;; 32 pages

jnc     bab                     ;; Iterate if necessary

lea     esi, [esi-32*4096]      ;; Next source pointer

; FFT levels 1-2 in place

mov     eax, 512                ;; 512 iterations

mov     ebp, esi

b1b:    test_disp test_macro, esi, 128, ebp, 16, 32, 64

lea     ebp, [ebp+128]

sub     eax, 1                  ;; Test inner loop counter

jnz     b1b                     ;; Iterate if necessary

; FFT levels 3-4 to scratch area

lea     esi, [esi-512*128]      ;; Next source pointer

b2a:    mov     ebp, OFFSET XMM_SCRATCH_AREA

b2b:    test_disp test_macro, esi, 32, ebp, 16, 256, 512

lea     ebp, [ebp+128]

add     al, 256/4               ;; Test inner loop counter

jnc     b2b                     ;; Iterate if necessary

prefetcht1 [esi-4*32+65536]

lea     esi, [esi-4*32+4*256]   ;; Next source pointer

add     cl, 256/4               ;; Test inner loop counter

jnc     b2b                     ;; Iterate if necessary

; FFT levels 5-6 from scratch area

lea     esi, [esi-16*256]       ;; Next source pointer

mov     ebp, OFFSET XMM_SCRATCH_AREA

b3b:    test_disp test_macro, ebp, 128, esi, 16, 32, 64

lea     esi, [esi+256]

add     al, 256/16

jnc     b3b

add     ah, 256/16              ;; 16 iterations

jnc     b2a                     ;; Iterate if necessary

lea     esi, [esi-256*256+128]  ;; Next source pointer

add     ch, 256/2               ;; 2 iterations

jnc     b2a                     ;; Iterate if necessary

; FFT levels 7-8 to scratch area

lea     esi, [esi-2*128]        ;; Next source pointer

b4a:    mov     ebp, OFFSET XMM_SCRATCH_AREA

b4b:    test_disp test_macro, esi, 32, ebp, 16, 256, 512

lea     ebp, [ebp+128]

add     al, 256/4               ;; Test inner loop counter

jnc     b4b                     ;; Iterate if necessary

prefetcht1 [esi-4*32+65536+256]

lea     esi, [esi-4*32+4*256]   ;; Next source pointer

add     cl, 256/4               ;; Test inner loop counter

jnc     b4b                     ;; Iterate if necessary

; FFT levels 9-10 from scratch area

lea     esi, [esi-16*256]       ;; Next source pointer

mov     ebp, OFFSET XMM_SCRATCH_AREA

b5b:    test_disp test_macro, ebp, 128, esi, 16, 32, 64

lea     esi, [esi+256]

add     al, 256/16

jnc     b5b

add     ah, 256/16              ;; 16 iterations

jnc     b4a                     ;; Iterate if necessary

lea     esi, [esi-256*256+128]  ;; Next source pointer

add     ch, 256/2               ;; 2 iterations

jnc     b4a                     ;; Iterate if necessary

; FFT levels 7-8 to scratch area

lea     esi, [esi-2*128]        ;; Next source pointer

b6a:    mov     ebp, OFFSET XMM_SCRATCH_AREA

b6b:    test_disp test_macro, esi, 32, ebp, 16, 256, 512

lea     ebp, [ebp+128]

add     al, 256/4               ;; Test inner loop counter

jnc     b6b                     ;; Iterate if necessary

prefetcht1 [esi-4*32+65536+512]

lea     esi, [esi-4*32+4*256]   ;; Next source pointer

add     cl, 256/4               ;; Test inner loop counter

jnc     b6b                     ;; Iterate if necessary

; FFT levels 5-6 from scratch area

lea     esi, [esi-16*256]       ;; Next source pointer

mov     ebp, OFFSET XMM_SCRATCH_AREA

b7b:    test_disp test_macro, ebp, 128, esi, 16, 32, 64

lea     esi, [esi+256]

add     al, 256/16

jnc     b7b

add     ah, 256/16              ;; 16 iterations

jnc     b6a                     ;; Iterate if necessary

lea     esi, [esi-256*256+128]  ;; Next source pointer

add     ch, 256/2               ;; 2 iterations

jnc     b6a                     ;; Iterate if necessary

; FFT levels 3-4 to scratch area

lea     esi, [esi-2*128]        ;; Next source pointer

b8a:    mov     ebp, OFFSET XMM_SCRATCH_AREA

b8b:    test_disp test_macro, esi, 32, ebp, 16, 256, 512

lea     ebp, [ebp+128]

add     al, 256/4               ;; Test inner loop counter

jnc     b8b                     ;; Iterate if necessary

prefetcht1 [esi-4*32+65536+768]

lea     esi, [esi-4*32+4*256]   ;; Next source pointer

add     cl, 256/4               ;; Test inner loop counter

jnc     b8b                     ;; Iterate if necessary

; FFT levels 1-2 from scratch area

lea     esi, [esi-16*256]       ;; Next source pointer

mov     ebp, OFFSET XMM_SCRATCH_AREA

b9b:    test_disp test_macro, ebp, 128, esi, 16, 32, 64

lea     esi, [esi+256]

add     al, 256/16

jnc     b9b

add     ah, 256/16              ;; 16 iterations

jnc     b8a                     ;; Iterate if necessary

lea     esi, [esi-256*256+128]  ;; Next source pointer

add     ch, 256/2               ;; 2 iterations

jnc     b8a                     ;; Iterate if necessary

lea     esi, [esi-2*128]        ;; Restore source pointer

ENDM

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Memory access pattern | Clocks for each xpass2 | Clocks per 64 byte cache line processed | Clocks per test_macro call | Comments |
| --- | --- | --- | --- | --- |
| 64KB in place | 199117 | 194.5 | 43.2 |  |
| 64KB main mem. | 222513 | 217.3 | 48.3 |  |

Since 128KB should easily fit in the cache and the prefetch instructions are spaced a good ways apart (at least 160 clocks), it is a little surprising that the prefetch does not completely eliminate the penalties of main memory access.

Next, I changed the first loop to prefetch lines that weren’t prefetched as hoped in processing the previous 64KB:

b1b:    test_disp test_macro, esi, 128, ebp, 16, 32, 64

is replaced with

b1b:    prefetcht1 [esi+8*128]

test_disp test_macro, esi, 128, ebp, 16, 32, 64

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Memory access pattern | Clocks for each xpass2 | Clocks per 64 byte cache line processed | Clocks per test_macro call | Comments |
| --- | --- | --- | --- | --- |
| 64KB in place | 199386 | 194.7 | 43.3 |  |
| 64KB main mem. | 214751 | 209.7 | 46.6 |  |

# Trace cache and branch prediction

I created a very simple loop and timed both the best case and average case of 200 calls to this code.  The results are quite puzzling:

mov     edx, 16384

loopy:  subsd   xmm0, xmm0

subsd   xmm0, xmm0

sub     edx, 1

jnz     loopy

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Best case | Average case | Comments |
| --- | --- | --- |
| 131280 | ~190000 | The average varies quite a bit. |

Conclusions:  Why would we not get 131,280 every time this code is executed.  On the second through 200th calls the entire loop should be in the trace cache.

Next, I tried flushing the trace cache by using self-modifying code prior to entering the loop:

trace_cache_flush MACRO

LOCAL   rrr

rrr:    mov     ds:BYTE PTR rrr, 0C6h

ENDM

mov     edx, 16384

trace_cache_flush

loopy:  subsd   xmm0, xmm0

subsd   xmm0, xmm0

sub     edx, 1

jnz     loopy

Timing for the above on a 1.4GHz P4 with PC600 memory:

| Best case | Average case | Comments |
| --- | --- | --- |
| 131780 | ~132400 | Much more consistent results |

Conclusion:  There is some kind of flaw in the trace cache design.  I’ve tried adding nops to the loop (when not flushing the trace cache) to see if more could be learned.  Depending on how many nops are added, you will get better averages, but in no case is the result as good as flushing the trace cache.

If you have loops that are not giving you consistent timings, this might be the cause.

# Tricks with SSE floating point exponents

In my FFT macros, I often need to multiply an XMM register by two.  At first I thought of two options:

ADDPD	xmm, xmm			;; Add register to itself

Or

XMM_TWO	DQ	2.0, 2.0

MULPD	xmm, XMM_TWO		;; Multiply by a global variable

I later thought of a third option:

XMM_INC_EXP DB	1,0,0,0,0,0,0,0,1,0,0,0,0,0,0,0

PADDB	xmm, XMM_INC_EXP	;; Add 1 to each exponent!

In my case the ADDPD option was unattractive because I was already doing a lot of ADDPDs and they can only be issued every other clock cycle.  The PADDB instruction is an attractive alternative to the MULPD instruction in that it has a shorter latency and makes it easier for the CPU to schedule other MULPD instructions.  Note:  I haven’t tested the above yet!

There are probably other opportunities for such optimizations.